## Slide 1: ICD-10 Coordination and Maintenance Committee Meeting Irreversible Electroporation A Treatment for Pancreatic and Liver Tumors March 18, 2015 Presented by: Robert C.G. Martin, II, MD, PhD, FACS

## Slide 2
Irreversible Electroporation A Treatment for Pancreatic and Liver Tumors
Sam and Lolita Weakley Endowed Chair in Surgical Oncology Director, Division of Surgical Oncology Director of the Upper GI and HPB Multi-Disciplinary Clinical Professor of Surgery Academic Advisory Dean University of Louisville
Robert C.G. Martin, II, MD, PhD, FACS
Disclosures: Paid consultant for AngioDynamics
March 18th, 2015

## Slide 3: Agenda
Coding Issue
Incidence & Statistics related to Pancreatic and Liver Cancer
About Irreversible Electroporation as a treatment for Pancreatic and Liver Cancer
Rationale for new ICD-10-PCS code
ICD-10-PCS Options
New Technology Add On Payment Application
Questions / Answers / Discussion

## Slide 4: Irreversible Electroporation (IRE)
Issue:
The Current ICD-10-PCS codes do not identify the specific technique that induces tumor cell membrane porosity thereby causing auto-programmed cancer cell death (i.e., apoptosis)
New Technology Add on Payment will be applied for in 2015 for consideration in 2017
Request new ICD-10-PCS code as soon as code freeze lifts
Avoid delays in tracking hospital cost and utilization data

## Slide 5
About Pancreatic and Liver Cancer

## Slide 6: Pancreatic Cancer is Projected to Become the 2nd Leading Cause of Cancer Death by 2020!
Pancreatic cancer is the fourth most common cause of death by cancer, but is on the rise
Pancreatic cancer is projected to become the 2nd leading cause of cancer death in the US by 2020
Siegel et al – CA Cancer J Clin 2013; Pancreatic Cancer Action Network 2012

## Slide 7: Pancreatic Cancer
5 Year Survival Data

## Slide 8: Pancreatic Cancer
Pancreatic Cancer Biology
45,000 cases diagnosed in 2012
10-20% patients will present with Resectable Stage II disease
  95% of these resected patients will recur in the next 5 years after their resection
  Most will relapse with metastatic disease
  Approx 30% will recur with only local disease
  Median interval: primary surgery and diagnosis recurrence 10.4 months (range 2.0-19.2 )
30-35% patients present with Locally Advanced Stage III disease
  Devastating disease with high mortality rate and overall 5 year survival rate lower than 5%
  Recently, an autopsy series of patients with pancreatic cancer identified 30% who succumbed to locally destructive disease without evidence of progression at distant sites
  Historically and nihilistically, with little foundation, little evidence, and with limited success chemo-radiotherapy alone has been and remains a component of LAPC therapy subsequent to a few small studies in the 1980s that used ineffective systemic therapies and older radiation techniques

## Slide 9: Liver Cancer
Liver Cancer Treatment Options
Complete surgical resection remains the most effective therapy for hepatic malignancy
Delays in diagnosis or poor underlying liver function mean that the number of patients who are candidates for this potentially curative approach is relatively small
In patients with HCC: 30–40% patients eligible for surgical resection
Non-surgical candidates with hepatic tumors may receive a liver directed therapy
  Radiofrequency ablation (RFA), ethanol ablation, laser ablation, cryoablation, high intensity focused ultrasound (HIFU), microwave ablation, and stereotactic body radiation therapy

## Slide 10: Liver Cancer
Thermal ablative technologies limitations: size & location limited the use and effectiveness of these modalities
  RFA studies have demonstrated that the rate of complete tumor necrosis falls below 50% when there are vessels larger than 3mm abutting the tumor, a consequence of the heat sink effect.
  Lesions in a sub capsular location or in close proximity to the gallbladder demonstrate similar difficulty in achieving complete ablation.
  Similar limitations around safety have also been demonstrated with the other thermal modalities in relation to lesions in proximity to vital structures (i.e., major bile ducts, portal vein, and hepatic veins).

## Slide 11
Irreversible Electroporation (IRE) as a treatment for pancreatic and liver cancers

## Slide 12: Irreversible Electroporation (IRE)
Series of short, low energy direct current electrical pulses
Does not rely on heat to ablate tissue
Creates defects – permanent pores in cell membranes
Cell death occurs by apoptosis
This immune mediated cell death allows cellular clearance of debris and creates minimal tissue distortion
3000 V @ d = 2.0 cm
A new treatment modality for locally advanced pancreatic & hepatic tumors

## Slide 13: Irreversible Electroporation (IRE)
Cell Exposure to Electric Field – Nano Sized Pore Formation
Exposure to an electric field may result either in permeabilization of cell membrane or its destruction
Temporary permeabilization can be described as Reversible Electroporation
Permanent permeabilization can be described as Irreversible Electroporation
Normal Liver
IRE with Nanopores

## Slide 14: Irreversible Electroporation (IRE)
Established Dose Response Curve

## Slide 15: Irreversible Electroporation (IRE)
Comparison of Biological Effects between Thermal Ablation and Irreversible Electroporation (IRE)
Effect | Thermal Ablation (RFA/Cryo/Microwave) | Irreversible Electroporation
Act of damage | Entire cell | Only cell membrane
Protein denaturation | Typical | Not present
Blood flow | Affects efficacy of ablation | No effect
Connective tissue | Damaged | Spared
Region of damage | Gradual change | Better defined
IHC effects | Present | Not present

## Slide 16: An IRE System
An IRE System Components
Generator
Single-use disposable electrodes
Features
19 gauge diameter
Up to 6 disposable electrodes may be used
Two electrode lengths available 15cm and 25cm

## Slide 17: The IRE System
IRE Probe Geometries
Customizable configurations for various tumor sizes
Two Probe Array
Three Probe Array
Four Probe Array
Six Probe Array

## Slide 18: Irreversible Electroporation (IRE)
Benefits: Precise Cellular Targeting
All cells in ablation zone are affected by electrical field- either transiently or permanently.
Fibrous and Collagen Structures are not affected
  Intact adventitia & laminae visible at 2 days with no smooth muscle cells present.
  Endothelium largely repopulates at 2 days.
  Smooth muscle repopulated at 2 weeks.

## Slide 19: Pre-Clinical Data Support IRE is Safe & Effective
Pre-Clinical IRE in Pancreas
Bower et al – Chronic animal study (14 days)
  No AE, All animals survived, no vascular thrombosis
  Complete ablation
Charpentier et al – Acute animal study (2 hours)
  No vascular thrombosis – complete ablation
Pre-Clinical IRE in Liver
Brown et al – Chronic animal study (4 days)
  Optimal probe spacing and number. no AE, effective
Charpentier et al – Acute animal study
  Safe

## Slide 20: IRE: Established Criteria
Evaluation of learning curve
Philips et al – IRE of Unresectable Soft Tissue Tumors: learning curve evaluation in the first 150 patients treated
Technical success
Defined as the ability to successfully deliver all planned accordance with the size and dimension of the lesion
Proximity to critical structures
Proximity to major vascular/biliary structures or adjacent organs was defined as <5mm in distance
Ablation recurrence
Persistent viable tumor as defined by dynamic imaging in comparison to pre-IRE scan or tissue diagnosis
Ablation success
The ability to deliver the planned therapy in the operative room and at 3 months to have no evidence of residual tumor on cross-sectional imaging of treating-team’s choice such as CT, MRI or PET (if pre-operative PET avid scan)

## Slide 21: Irreversible Electroporation (IRE)
Current Clinical Use of IRE in the Pancreas
Treat locally advanced pancreatic cancer (80% use) – Stage III
Margin accentuation/augmentation therapy (10% use) – Stage IIb
  After patient has undergone appropriate neo-adjuvant therapy
Treat local recurrent cancer (5% use)
Metastatic disease to pancreas (5% use)

## Slide 22: Irreversible Electroporation (IRE)
Benefits of IRE in Pancreas
Can be performed in conjunction with pancreatic resection
Can be utilized to augment any margin that is considered to be close or positive R1
No thermal based modality has demonstrated Safety or Efficacy
Only current modality that is used is XRT
  Best reported recurrence rate of 4-8%, median OS in Stage III LAPC is 9 months (4-11months)

## Slide 23: Irreversible Electroporation (IRE)
Benefits of IRE in the Liver
The ability to achieve ablation without damage to surrounding vital structures
No evidence of heat sink effect despite close proximity to major vascular structures
No evidence of damage to the portal triad structures
IRE has a suitable role in the treatment of patients who are less than ideal candidates for current thermal ablation modalities due to tumor location in proximity to vital structures

## Slide 24: Clinical Experience with IRE for Margin Accentuation
Methods
Patients with pancreatic cancer who underwent pancreatectomy with margin accentuation with IRE were followed in a prospective IRE approved database from 7/2010 to 7/2013
Data regarding local recurrence, margin status, and survival were evaluated
Results
48 patients underwent pancreatectomy
  Pancreaticoduodenectomy (58%), subtotal pancreatectomy (35%), distal pancreatectomy (4%), and total pancreatectomy (4%)
IRE margin accentuation of the superior mesenteric artery and/or the anterior margin of the aorta
All patients underwent induction therapy
  25 patients had chemo-radiation therapy, 18 patients had chemotherapy, for a median duration of 6 months (4-13) prior to resection
A majority (54%) required vascular resection

## Slide 25: Clinical Experience with IRE for Margin Accentuation
Results
Total of 9 (19%) patients, sustained 21 complications with median grade of 2 (range 1-3)
Median length of stay of 7 days (range 4-58)
Median FU of 24 months, 3 (6%) have local recurrence, with a median survival of 23.5 months
Conclusions
Simultaneous intra-operative IRE and pancreatectomy can provide an adjunct to resection in patients with locally advanced disease
Long-term follow up has demonstrated a small local recurrence rate that is far below expected
Continued optimization in multi-modality therapy and consideration of appropriate patients could translate into a larger subset that could be effectively treated

## Slide 26: Clinical Experience with IRE for Stage III LAPC
Methods
Patients with stage III locally advanced pancreatic cancer who underwent IRE for unresectable pancreatic cancer were followed in a prospective IRE approved database from 12/2009 to 10/2010 was evaluated for overall survival and propensity marched to 85 matched stage III patients treated with standard therapy (Chemo or XRT)

## Slide 27: Clinical Experience with IRE for Stage III LAPC
Results
54 patients underwent IRE successfully
  21 women, 23 men, median age 61 (range 45-80)
  Pancreatic head (35 patients), Pancreatic Body/Neck (19 patients)
  19 patients underwent margin accentuation with IRE, 35 underwent in-situ ablation with IRE
49 patients (90%) had pre-IRE chemotherapy alone or chemoradiation therapy for a median duration of 5 months
40 patients (73%) underwent post-IRE chemotherapy or chemoradiation

## Slide 28: Clinical Experience with IRE for Stage III LAPC
Results
90 day mortality in the IRE patients was 1 (2%)
Comparing IRE patients to standard therapy, we have seen improvement in:
  Local progression-free survival
    (14 vs. 6 months, p=0.01)
  Distant progression-free survival
    (15 vs. 9 months, p=0.02)
  Overall survival
    (20 vs. 13 months, p=0.03)

## Slide 29: Clinical Experience with IRE for Stage III LAPC
Conclusions
IRE ablation of locally advanced pancreatic tumors remains safe and in the appropriate patient who has undergone standard induction therapy for a minimum of 4 months can achieve greater local palliation and potential improved overall survival compared with standard chemoradiation-chemotherapy treatments

## Slide 30: Clinical Experience with IRE in Liver
Methods
Patients undergoing IRE for hepatic tumors were followed on an IRB approved prospective registry over a 2-year period and evaluated for safety and efficacy
Factors analyzed included patient and tumor characteristics, treatment related complications, and local recurrence free survival (LRFS) for ablated lesions

## Slide 31: Clinical Experience with IRE in Liver
Results
44 patients underwent 48 total IRE procedures successfully
  20 colorectal mets, 14 hepatocellular, and 10 other metastatsis
Five patients had 9 adverse events, with all complications resolving within 30 days
LRFS at 3, 6, and 12 months was 97.4%, 94.6%, and 59.5%.
There was a trend toward higher recurrence rates for tumors over 4 cm
  (HR 3.236, 95% CI: 0.585–17.891; P ¼ 0.178)
Conclusions
IRE appears to be a safe treatment for hepatic tumors in proximity to vital structures

## Slide 32: ICD-10-PCS Rationale for Irreversible Electroporation, IRE
Under Current ICD-10-PCS codes ablation is a term included in the root operation Destruction as, “physical eradication of all or a portion of a body part by the direct use of energy, force or destructive agent”
The current ICD-10-PCS codes do not identify the specific technique that induces tumor cell membrane porosity thereby causing auto-programmed cancer cell death (i.e., apoptosis)
Having unique codes to distinctly identify Irreversible Electroporation (IRE) procedures will enable:
Tracking and measurement of utilization
Tracking clinically meaningful outcomes measurements
Clear procedural code option for hospital coders
Unique codes will help differentiate between Irreversible Electroporation (IRE) and thermal ablative modalities to allow for essential data collection

## Slide 33: ICD-10-PCS Committee Preliminary Code Options
OPTION | DESCRIPTION | COMMENT
Option 1 | Do not create new codes for IRE | This option does not enable a means to capture the IRE procedure.
Option 2 | Create qualifier F (IRE) in character 7 of section 0F5 to identify IRE versus other destruction techniques | We support this option as this will provide a means to capture the use of IRE. This option makes sense and is logical as it is within the same root operation as other destructive techniques.
Option 3 | Create new codes in section X New Technology to identify the IRE destruction technique | We do not support this option as this there is not enough information on this New Technology option.

## Slide 34: Clinical Questions?