## Slide 1: ICD-10-PCS Meeting 3/18/15 VERASENSE™
Gregory J. Golladay, MD
Associate Professor Orthopedic Surgery
Virginia Commonwealth University Medical Center

## Slide 2: ISSUE: VERASENSE™ KNEE BALANCER SYSTEM INSERTION
FDA cleared
Sterile, single use, disposable after insertion into the open tibial plateau during total knee arthroplasty (TKA)
Intelligent instrument- embedded with micro-processing chip, proprietary sensors, accelerometer and RF technology
Enables surgeon to quantify center of load and kinetic tracking of load
Assists surgeon establishing optimal implant ROTATION and soft tissue BALANCE
Compatible with Stryker, Zimmer, Biomet & Smith & Nephew Total Knee Systems

## Slide 3: ISSUE: MEDICALLY NECESSARY FOR IMPROVED IMPLANT PLACEMENT THE JOURNAL OF ARTHROPLASTY SURGEON POLL (2014)

## Slide 4: Background: Technology and Procedure
VERASENSE™ Intelligent Tibial Trial
Detects and quantifies rotational congruency and intercompartmental load differential during TKA.
Measures TKA kinematic performance (no other technology currently available in market)
Evidence of improved patient outcomes
  More than 7 peer-reviewed publications
  Demonstrating statistically significant TKA clinical and functional outcome scores over conventional or navigated TKA techniques.

## Slide 5: After initial trialing, ROM is completed, and the surgeon inserts the intelligent tibial trial into the open knee compartment to rest on the tibial plateau and activated.
PROCEDURE: INSERTION OF INTELLIGENT TIBIAL TRIAL

## Slide 6: Insertion requires added surgeon work and training with no change in surgical workflow. There is no piercing of tissue or bone.
PROCEDURE: INSERTION OF INTELLIGENT TIBIAL TRIAL

## Slide 7: Quantitative Load and Balance Measurements Through ROM to Guide Surgeons tissue dissection.

## Slide 8
INFORMATION TO THE SURGEON
KINETIC TRACKING FULL ROM

## Slide 9
High lateral compartment pressures near full extension (note 2.5° varus mechanical alignment.
Compartment pressures more equalized after 3° valgus recut of the distal femur.
SURGEON’S RESPONSE TO QUANTIFIED BALANCE:
Full ROM

## Slide 10: Initial trialing identified tight medial soft-tissues causing elevated medial compartment pressures. Compartment pressures are more equalized after a medial soft-tissue release. (Gustke 2014)

## Slide 11: IMPROVED TKA IMPLANT PLACEMENT Studies have demonstrated knees with <15 lb. mediolateral pressure differential have statistically significant higher KSS function scores than unbalanced knees
Regression analysis divided into 5 lbs. of mediolateral (ML) difference (0-5, 5-10, 10-15, etc.) was conducted to understand where patients experienced the greatest gains or reductions in Knee Society Scores (KSS).

## Slide 12: STANDARDIZED OUTCOME MEASURES Multicenter Study Results at 6-month, 1-year, 2-year intervals
Chart: KSS Pain
| Pre-Op | 6 Months | 1 Year | 2 Year
Balanced | 54.2 | 91.2 | 96.4 | 94
Unbalanced | 54.2 | 81.2 | 87.8 | 88
Chart: KSS Function
| Pre-Op | 6 Months | 1 Year | 2 Year
Balanced | 52.6 | 79.3 | 82.4 | 80.7
Unbalanced | 52.6 | 61 | 68.3 | 73.8
Chart: WOMAC
| Pre-Op | 6 Months | 1 Year | 2 Year
Balanced | 53.7 | 85.5 | 89.6 | 89
Unbalanced | 53.7 | 76.2 | 82.1 | 82.4
Chart: Activity Level
| Pre-Op | 6 Months | 1 Year | 2 Year
Balanced | 43.5 | 60.2 | 68.6 | 66.8
Unbalanced | 43.5 | 48 | 46.7 | 50

## Slide 13: STANDARDIZED OUTCOME MEASURES Multicenter Study Results at 6-month, 1-year, 2-year intervals

## Slide 14: Verasense Intra-compartmental Insertion and Surgeon’s Response to Load and Balance Metrics Leads to Improved TKA Implant Placement
Insertion of the Verasense TM Intelligent Tibial Trial
Is a novel surgical aspect of TKA.
Offers the ability to diagnose improper implant placement
Enables the surgeon to take immediate corrective action
Improved implant stability and balance reduces the probability of a knee revision surgery supported by 3 years of clinical evidence.
Key Criteria for a new ICD-10-PCS code
No current ICD-10-PCS code exists for this novel procedure performed during TKA, but distinctly separate from conventional TKA.
Entirely new procedure with distinct beginning, middle and end.
Device has novelty and leads to Improved Patient Outcomes.
The concept of “balanced” TKA able to prevent rotational incongruency is due to the Verasense TM Knee Balancer System.

## Slide 15: Clinical Evidence of Significant Improvement In TKA Outcomes
A distinct ICD-10-PCS code is needed
Novel new procedure
Need utilization tracking
Need to follow patient outcome
Accuracy of rotational congruency can be achieved with the improved balance measurements
Published Evidence: Study comparing the internal rotation of VERASENSETM Balanced TKA to conventional methods using the tibial tubercle as a point of reference, and then correcting the rotational incongruency resulted in the avoidance of anterior knee pain manifesting in as much as 35% of the conventionally treated patient group (those with incongruency ≥6.2°). Roche MW, et. al. A Novel Technique Using Sensor-Based Technology to Evaluate Tibial Tray Rotation. Orthopedics. 2014 (In Press)

## Slide 16: Clinical Evidence of Significant Improvement In TKA Outcomes
Published Evidence: Barrack reported that as little as 6.2° of internal rotation (IR) of the tibial component is associated with postoperative anterior knee pain with time resulting in revision TKA. Barrack RL, et.al. Component rotation and anterior knee pain after total knee arthroplasty. Clin Orthop Rel Res 2001;392:46-55.
Conclusion: Patient complications were avoided due to implant rotation/balance/congruency correction, based on the metrics provided by the VERASENSETM System used intraoperatively placed within the open knee compartment. Roche MW, Elson LC, Anderson CR, A novel technique using sensor-based technology to evaluate tibial tray rotation. Orthopedics, 2014 in press

## Slide 17: Balanced Knees: Deliver Cost Effective TKA Outcomes
VERASENSETM Procedure Results in
Decreased rate of subsequent diagnostic or therapeutic interventions (for example, due to reduced rate of revision or other interventions)
    Balanced Cohort Did Not Require Emergent or Problem Focused Follow up Visits
Decreased number of future hospitalizations or physician visits
    Roche et al. (2014) demonstrated 35% of TKA are at risk for a revision or readmission due to incongruence of rotation.
    The VerasenseTM procedure corrects this problem.
    Balanced TKA will reduce the incidence of Readmission for TKA. 71.5% of 159,840 Hip and Knee Readmissions in 2013. (MS-DRG readjustment factor HK 2013 and CDC Faststats http://www.cdc.gov/nchs/fastats/inpatient-surgery.htm).

## Slide 18: Verasense TM Knee Balancer System Improved Outcomes is Cost Effective
TKA is growing rapidly increasing in the Medicare population to 243,802 in 2010 a 161.5% increase from 1991. (P. Cram, et. al. Total knee arthroplasty volume, utilization, and outcomes among Medicare Beneficiaries, 1991-2010. JAMA. 2012;308(12):1227-1236.)
2010 there were 19,871 Revision TKA with mean cost of $27,000 (NIS 2012 ICD-9-CM 00.80)
Roche reported 35% of the “unbalanced” TKA could result in a revision.
Estimating a 50% reduction in the incidence of the 35% at risk for revision TKA (0.175*19,871)=3,477 revision TKA avoided approximates to
Annualized CMS savings of $93,879,000.

## Slide 19: Outcome Metrics: Leads to Statistically Significant Improvement
Rapid recovery because of the use of the device (balanced knees are better at 6 months than unbalanced knees at 2 years)
Decreased pain, stiffness, instability and other quantifiable symptoms
Continued functional improvement over time (balanced knees continue to show increased function between 6, 12 months and 2 years, while unbalanced knees plateau)
Outcomes Measured Using Standardized Metrics
American Knee Society Score (KSS)
Western Ontario and McMaster Universities Osteoarthritis Index (WOMAC)
Patient Satisfaction & Activity Level Scores

## Slide 20: Outcome Metrics: Meet Significant Improvement Criterion
Balanced TKA patients at 2 years report “satisfied” to “very satisfied” 98% vs 81% of patients with unbalanced knees.
This represents nearly 21% (17/81) improvement in patient satisfaction (P<0.001).
Patient outcome data report a significant improvement over routine TKA or navigated TKA in functional outcome measures, activity level and reduction in BMI.
Mackie A, et al, Association Between Body Mass Index Change and Outcome in the First Year After Total Knee Arthroplasty, J Arthroplasty (2014), http://dx.doi.org/10.1016/j.arth.2014.09.003
Golladay GJ, Jerry GJ, Gustke KA, Roche MW, Elson L, Anderson C. Post-operative weight gain after total knee arthroplasty: Prevalence and its possible attenuation using intraoperative sensors. Reconstructive Review 2014 March Vol 4, No 138-41.
Jerry G, Dounchis J, Computer-Assisted Orthopaedic Surgery During TKA Is Insufficient for Ensuring Ideal Joint Reconstruction:, Bone Joint J (2013).
Roche MW, Elson LC, Anderson CR, A Novel Technique Using Sensor-Based Technology to Evaluate Tibial Tray Rotation. Orthopedics. 2014 (In Press)

## Slide 21: Patient-Reported Satisfaction: Also Statistically Significant- Improved

## Slide 22: Outcome Measures: Superior to Conventional and/or CAOS
Outcome Measure | Variable Score Change Between Preop and 6 mo (p<0.001) | Odds Ratio
KSS | Δ N + 50 pts | 2.5
WOMAC | Δ N + 30 pts | 1.3
Activity Level | Δ N + 40 pts | 1.8
Odds Ratios: Likelihood of Balanced Patients Achieving Clinically Meaningful Improvement Over Unbalanced Patients.
Jerry G, Dounchis J, Computer-Assisted Orthopaedic Surgery During TKA Is Insufficient for Ensuring Ideal Joint Reconstruction:, Bone Joint J (2013) http://www.bjjprocs.boneandjoint.org.uk/content/95-B/SUPP_34/356.short.
Roche MW, Elson LC, Anderson CR, A Novel Technique Using Sensor-Based Technology to Evaluate Tibial Tray Rotation. Orthopedics. 2014 (In Press)